## Slide 1: Digital Integrated Circuits A Design Perspective
Introduction
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolic
July 30, 2002

## Slide 2: What is this book all about?
Introduction to digital integrated circuits.
  CMOS devices and manufacturing technology. CMOS inverters and gates. Propagation delay, noise margins, and power dissipation. Sequential circuits. Arithmetic, interconnect, and memories. Programmable logic arrays. Design methodologies.
What will you learn?
  Understanding, designing, and optimizing digital circuits with respect to different quality metrics: cost, speed, power dissipation, and reliability

## Slide 3: Digital Integrated Circuits
Introduction: Issues in digital design
The CMOS inverter
Combinational logic structures
Sequential logic gates
Design methodologies
Interconnect: R, L and C
Timing
Arithmetic building blocks
Memories and array structures

## Slide 4: Introduction
Why is designing digital ICs different today than it was before?
Will it change in future?

## Slide 5: The First Computer

## Slide 6: ENIAC - The first electronic computer (1946)

## Slide 7: The Transistor Revolution
First transistor
Bell Labs, 1948

## Slide 8: The First Integrated Circuits
Bipolar logic
1960’s
ECL 3-input Gate
Motorola 1966

## Slide 9: Intel 4004 Micro-Processor
1971
1000 transistors
1 MHz operation

## Slide 10: Intel Pentium (IV) microprocessor

## Slide 11: Moore’s Law
In 1965, Gordon Moore noted that the number of transistors on a chip doubled every 18 to 24 months.
He made a prediction that semiconductor technology will double its effectiveness every 18 months

## Slide 12: Moore’s Law
Electronics, April 19, 1965.

## Slide 13: Evolution in Complexity

## Slide 14: Transistor Counts
1,000,000
100,000
10,000
1,000
10
100
1
1975
1980
1985
1990
1995
2000
2005
2010
8086
80286
i386
i486
Pentium®
Pentium® Pro
K
1 Billion Transistors
Source: Intel
Projected
Pentium® II
Pentium® III
Courtesy, Intel

## Slide 15: Moore’s law in Microprocessors
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
P6
0.001
0.01
0.1
1
10
100
1000
1970
1980
1990
2000
2010
Year
Transistors (MT)
2X growth in 1.96 years!
Transistors on Lead Microprocessors double every 2 years
Courtesy, Intel

## Slide 16: Die Size Growth
4004
8008
8080
8085
8086
286
386
486
Pentium ® proc
P6
1
10
100
1970
1980
1990
2000
2010
Year
Die size (mm)
~7% growth per year
~2X growth in 10 years
Die size grows by 14% to satisfy Moore’s Law
Courtesy, Intel

## Slide 17: Frequency
P6
Pentium ® proc
486
386
286
8086
8085
8080
8008
4004
0.1
1
10
100
1000
10000
1970
1980
1990
2000
2010
Year
Frequency (Mhz)
Lead Microprocessors frequency doubles every 2 years
Doubles every 2 years
Courtesy, Intel

## Slide 18: Power Dissipation
P6
Pentium ® proc
486
386
286
8086
8085
8080
8008
4004
0.1
1
10
100
1971
1974
1978
1985
1992
2000
Year
Power (Watts)
Lead Microprocessors power continues to increase
Courtesy, Intel

## Slide 19: Power will be a major problem
5KW
18KW
1.5KW
500W
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
0.1
1
10
100
1000
10000
100000
1971
1974
1978
1985
1992
2000
2004
2008
Year
Power (Watts)
Power delivery and dissipation will be prohibitive
Courtesy, Intel

## Slide 20: Power density
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
P6
1
10
100
1000
10000
1970
1980
1990
2000
2010
Year
Power Density (W/cm2)
Hot Plate
Nuclear
Reactor
Rocket
Nozzle
Power density too high to keep junctions at low temp
Courtesy, Intel

## Slide 21: Not Only Microprocessors
Digital Cellular Market
(Phones Shipped)
1996 1997 1998 1999 2000
Units 48M 86M 162M 260M 435M
Analog
Baseband
Digital Baseband
(DSP + MCU)
Power
Management
Small
Signal RF
Power
RF
(data from Texas Instruments)
Cell Phone

## Slide 22: Challenges in Digital Design
“Microscopic Problems”
• Ultra-high speed design
Interconnect
• Noise, Crosstalk
• Reliability, Manufacturability
• Power Dissipation
• Clock distribution.
Everything Looks a Little Different
“Macroscopic Issues”
• Time-to-Market
• Millions of Gates
• High-Level Abstractions
• Reuse & IP: Portability
• Predictability
• etc.
…and There’s a Lot of Them!
µ DSM
µ 1/DSM
?

## Slide 23: Productivity Trends
1
10
100
1,000
10,000
100,000
1,000,000
10,000,000
2003
1981
1983
1985
1987
1989
1991
1993
1995
1997
1999
2001
2005
2007
2009
10
100
1,000
10,000
100,000
1,000,000
10,000,000
100,000,000
Logic Tr./Chip
Tr./Staff Month.
x
x
x
x
x
x
x
21%/Yr. compound
Productivity growth rate
x
58%/Yr. compounded
Complexity growth rate
10,000
1,000
100
10
1
0.1
0.01
0.001
Logic Transistor per Chip
(M)
0.01
0.1
1
10
100
1,000
10,000
100,000
Productivity
(K) Trans./Staff - Mo.
Source: Sematech
Complexity outpaces design productivity
Complexity
Courtesy, ITRS Roadmap

## Slide 24: Why Scaling?
Technology shrinks by 0.7/generation
With every generation can integrate 2x more functions per chip; chip cost does not increase significantly
Cost of a function decreases by 2x
But …
  How to design chips with more and more functions?
  Design engineering population does not double every two years…
Hence, a need for more efficient design methods
  Exploit different levels of abstraction

## Slide 25: Design Abstraction Levels
n+
n+
S
G
D
+
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM

## Slide 26: Design Metrics
How to evaluate performance of a digital circuit (gate, block, …)?
  Cost
  Reliability
  Scalability
  Speed (delay, operating frequency)
  Power dissipation
  Energy to perform a function

## Slide 27: Cost of Integrated Circuits
NRE (non-recurrent engineering) costs
  design time and effort, mask generation
  one-time cost factor
Recurrent costs
  silicon processing, packaging, test
  proportional to volume
  proportional to chip area

## Slide 28: NRE Cost is Increasing

## Slide 29: Die Cost
Single die
Wafer
From http://www.amd.com
Going up to 12” (30cm)

## Slide 30: Cost per Transistor
0.0000001
0.000001
0.00001
0.0001
0.001
0.01
0.1
1
1982
1985
1988
1991
1994
1997
2000
2003
2006
2009
2012
cost:
¢-per-transistor
Fabrication capital cost per transistor (Moore’s law)

## Slide 31: Yield

## Slide 32: Defects
a is approximately 3

## Slide 33: Some Examples (1994)
Chip | Metal layers | Line width | Wafer cost | Def./ cm2 | Area mm2 | Dies/wafer | Yield | Die cost
386DX | 2 | 0.90 | $900 | 1.0 | 43 | 360 | 71% | $4
486 DX2 | 3 | 0.80 | $1200 | 1.0 | 81 | 181 | 54% | $12
Power PC 601 | 4 | 0.80 | $1700 | 1.3 | 121 | 115 | 28% | $53
HP PA 7100 | 3 | 0.80 | $1300 | 1.0 | 196 | 66 | 27% | $73
DEC Alpha | 3 | 0.70 | $1500 | 1.2 | 234 | 53 | 19% | $149
Super Sparc | 3 | 0.70 | $1700 | 1.6 | 256 | 48 | 13% | $272
Pentium | 3 | 0.80 | $1500 | 1.5 | 296 | 40 | 9% | $417

## Slide 34: Reliability― Noise in Digital Integrated Circuits
i
(
t
)
Inductive coupling
Capacitive coupling
Power and ground
noise
v
(
t
)
V
DD

## Slide 35: DC Operation Voltage Transfer Characteristic
V(x)
V(y)
V
OH
V
OL
V
M
V
OH
V
OL
f
V(y)=V(x)
Switching Threshold
Nominal Voltage Levels
VOH = f(VOL)
VOL = f(VOH)
VM = f(VM)

## Slide 36: Mapping between analog and digital signals
V
IL
V
IH
V
in
Slope = -1
Slope = -1
V
OL
V
OH
V
out
“
0
”
V
OL
V
IL
V
IH
V
OH
Undefined
Region
“
1
”

## Slide 37: Definition of Noise Margins
Noise margin high
Noise margin low
V
IH
V
IL
Undefined Region
"1"
"0"
V
OH
V
OL
NM
H
NM
L
Gate Output
Gate Input

## Slide 38: Noise Budget
Allocates gross noise margin to expected sources of noise
Sources: supply noise, cross talk, interference, offset
Differentiate between fixed and proportional noise sources

## Slide 39: Key Reliability Properties
Absolute noise margin values are deceptive
  a floating node is more easily disturbed than a node driven by a low impedance (in terms of voltage)
Noise immunity is the more important metric – the capability to suppress noise sources
Key metrics: Noise transfer functions, Output impedance of the driver and input impedance of the receiver;

## Slide 40: Regenerative Property
Regenerative
Non-Regenerative

## Slide 41: Regenerative Property
A chain of inverters
v
0
v
1
v
2
v
3
v
4
v
5
v
6
Simulated response

## Slide 42: Fan-in and Fan-out
N
Fan-out N
Fan-in M
M

## Slide 43: The Ideal Gate
R
i
=
¥
R
o
= 0
Fanout = ¥
NMH = NML = VDD/2
g = 
V
in
V
out

## Slide 44: An Old-time Inverter
NM
H
V
in
(V)
V
out
(V)
NM
L
V
M
0.0
1.0
2.0
3.0
4.0
5.0
1.0
2.0
3.0
4.0
5.0

## Slide 45: Delay Definitions

## Slide 46: Ring Oscillator
T = 2
´
t
p
´
N

## Slide 47: A First-Order RC Network
v
out
v
in
C
R
tp = ln (2) t = 0.69 RC
Important model – matches delay of inverter

## Slide 48: Power Dissipation
Instantaneous power:
p(t) = v(t)i(t) = Vsupplyi(t)
Peak power:
Ppeak = Vsupplyipeak
Average power:

## Slide 49: Energy and Energy-Delay
Power-Delay Product (PDP) = E = Energy per operation = Pav  tp
Energy-Delay Product (EDP) = quality metric of gate = E  tp

## Slide 50: A First-Order RC Network
v
out
v
in
CL
R

## Slide 51: Summary
Digital integrated circuits have come a long way and still have quite some potential left for the coming decades
Some interesting challenges ahead
  Getting a clear perspective on the challenges and potential solutions is the purpose of this book
Understanding the design metrics that govern digital design is crucial
  Cost, reliability, speed, power and energy dissipation