## Slide 1: Digital Integrated Circuits A Design Perspective
The Inverter
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolic
July 30, 2002

## Slide 2: The CMOS Inverter: A First Glance
V
in
V
out
C
L
V
DD

## Slide 3: CMOS Inverter
Polysilicon
In
Out
V
DD
GND
PMOS
2l
Metal 1
NMOS
Contacts
N Well

## Slide 4: Two Inverters
Connect in Metal
Share power and ground
Abut cells

## Slide 5: CMOS Inverter First-Order DC Analysis
VOL = 0
VOH = VDD
VM = f(Rn, Rp)
V
DD
V
DD
V
in
5
V
DD
V
in
5
0
V
out
V
out
R
n
R
p

## Slide 6: CMOS Inverter: Transient Response
t
pHL
= f(R
on
.C
L
)
= 0.69 R
on
C
L
V
out
V
out
R
n
R
p
V
DD
V
DD
V
in
5
V
DD
V
in
5
0
(a) Low-to-high
(b) High-to-low
C
L
C
L

## Slide 7: Voltage Transfer Characteristic

## Slide 8: PMOS Load Lines
V
DSp
I
Dp
V
GSp
=-2.5
V
GSp
=-1
V
DSp
I
Dn
V
in
=0
V
in
=1.5
V
out
I
Dn
V
in
=0
V
in
=1.5
V
in
= V
DD
+V
GSp
I
Dn
= - I
Dp
V
out
= V
DD
+V
DSp
V
out
I
Dn
V
in
= V
DD
+V
GSp
I
Dn
= - I
Dp
V
out
= V
DD
+V
DSp

## Slide 9: CMOS Inverter Load Characteristics

## Slide 10: CMOS Inverter VTC

## Slide 11: Switching Threshold as a function of Transistor Ratio
10
0
10
1
0.8
0.9
1
1.1
1.2
1.3
1.4
1.5
1.6
1.7
1.8
M
V
(V)
W
p
/W
n

## Slide 12: Determining VIH and VIL
V
OH
V
OL
V
in
V
out
V
M
V
IL
V
IH
A simplified approach

## Slide 13: Inverter Gain

## Slide 14: Gain as a function of VDD
Gain=-1

## Slide 15: Simulated VTC

## Slide 16: Impact of Process Variations
0
0.5
1
1.5
2
2.5
0
0.5
1
1.5
2
2.5
V
in
(V)
V
out
(V)
Good PMOS
Bad NMOS
Good NMOS
Bad PMOS
Nominal

## Slide 17: Propagation Delay

## Slide 18: CMOS Inverter Propagation Delay Approach 1

## Slide 19: CMOS Inverter Propagation Delay Approach 2

## Slide 20: CMOS Inverters
Polysilicon
In
Out
Metal1
V
DD
GND
PMOS
NMOS
1.2
m
m
=2l

## Slide 21: Transient Response
tp = 0.69 CL (Reqn+Reqp)/2
?
tpLH
tpHL

## Slide 22: Design for Performance
Keep capacitances small
Increase transistor sizes
  watch out for self-loading!
Increase VDD (????)

## Slide 23: Delay as a function of VDD

## Slide 24: Device Sizing
(for fixed load)
Self-loading effect:
Intrinsic capacitances
dominate

## Slide 25: NMOS/PMOS ratio
tpLH
tpHL
tp
b = Wp/Wn

## Slide 26: Impact of Rise Time on Delay

## Slide 27: Inverter Sizing

## Slide 28: Inverter Chain
CL
If CL is given:
How many stages are needed to minimize the delay?
How to size the inverters?
May need some additional constraints.
In
Out

## Slide 29: Inverter Delay
Minimum length devices, L=0.25mm
Assume that for WP = 2WN =2W
  same pull-up and pull-down currents
  approx. equal resistances RN = RP
  approx. equal rise tpLH and fall tpHL delays
Analyze as an RC network
tpHL = (ln 2) RNCL
tpLH = (ln 2) RPCL
Delay (D):
2W
W
Load for the next stage:

## Slide 30: Inverter with Load
Load (CL)
Delay
Assumptions: no load -> zero delay
CL
tp = k RWCL
RW
RW
Wunit = 1
k is a constant, equal to 0.69

## Slide 31: Inverter with Load
Load
Delay
Cint
CL
Delay = kRW(Cint + CL) = kRWCint + kRWCL = kRW Cint(1+ CL /Cint)
= Delay (Internal) + Delay (Load)
CN = Cunit
CP = 2Cunit
2W
W

## Slide 32: Delay Formula
Cint = gCgin with g  1
f = CL/Cgin - effective fanout
R = Runit/W ; Cint =WCunit
tp0 = 0.69RunitCunit

## Slide 33: Apply to Inverter Chain
CL
In
Out
1
2
N
tp = tp1 + tp2 + …+ tpN

## Slide 34: Optimal Tapering for Given N
Delay equation has N - 1 unknowns, Cgin,2 – Cgin,N
Minimize the delay, find N - 1 partial derivatives
Result: Cgin,j+1/Cgin,j = Cgin,j/Cgin,j-1
Size of each stage is the geometric mean of two neighbors
each stage has the same effective fanout (Cout/Cin)
each stage has the same delay

## Slide 35: Optimum Delay and Number of Stages
When each stage is sized by f and has same eff. fanout f:
Minimum path delay
Effective fanout of each stage:

## Slide 36: Example
CL= 8 C1
In
Out
C1
1
f
f2
CL/C1 has to be evenly distributed across N = 3 stages:

## Slide 37: Optimum Number of Stages
For a given load, CL and given input capacitance Cin
Find optimal sizing f
For g = 0, f = e, N = lnF

## Slide 38: Optimum Effective Fanout f
Optimum f for given process defined by g
fopt = 3.6
for g=1

## Slide 39: Impact of Self-Loading on tp
No Self-Loading, g=0
With Self-Loading g=1

## Slide 40: Normalized delay function of F

## Slide 41: Buffer Design
1
1
1
1
8
64
64
64
64
4
2.8
8
16
22.6
N f tp
1 64 65
2 8 18
3 4 15
4 2.8 15.3

## Slide 42: Power Dissipation

## Slide 43: Where Does Power Go in CMOS?

## Slide 44: Dynamic Power Dissipation
Energy/transition = C
L
* V
dd
2
Power = Energy/transition *
f =
C
L
* V
dd
2
* f
Need to reduce C
L
, V
dd
, and
f
to reduce power.
Vin
Vout
C
L
Vdd
Not a function of transistor sizes!

## Slide 45
Modification for Circuits with Reduced Swing

## Slide 46
Adiabatic Charging
2
2
2

## Slide 47
Adiabatic Charging

## Slide 48
Node Transition Activity and Power

## Slide 49: Transistor Sizing for Minimum Energy
Goal: Minimize Energy of whole circuit
  Design parameters: f and VDD
  tp  tpref of circuit with f=1 and VDD =Vref

## Slide 50: Transistor Sizing (2)
Performance Constraint (g=1)
Energy for single Transition

## Slide 51: Transistor Sizing (3)
F=1
2
5
10
20
VDD=f(f)
E/Eref=f(f)

## Slide 52
Short Circuit Currents

## Slide 53
How to keep Short-Circuit Currents Low?
Short circuit current goes to zero if tfall >> trise,
but can’t do this for cascade logic, so ...

## Slide 54
Minimizing Short-Circuit Power
Vdd =1.5
Vdd =2.5
Vdd =3.3

## Slide 55
Leakage
Sub-threshold current one of most compelling issues
in low-energy circuit design!

## Slide 56
Reverse-Biased Diode Leakage
JS = 10-100 pA/mm2 at 25 deg C for 0.25mm CMOS
JS doubles for every 9 deg C!

## Slide 57
Subthreshold Leakage Component

## Slide 58
Static Power Consumption
Wasted energy …
Should be avoided in almost all cases,
but could help reducing energy in others (e.g. sense amps)

## Slide 59: Principles for Power Reduction
Prime choice: Reduce voltage!
  Recent years have seen an acceleration in supply voltage reduction
  Design at very low voltages still open question (0.6 … 0.9 V by 2010!)
Reduce switching activity
Reduce physical capacitance
  Device Sizing: for F=20
    fopt(energy)=3.53, fopt(performance)=4.47

## Slide 60: Impact of Technology Scaling

## Slide 61: Goals of Technology Scaling
Make things cheaper:
  Want to sell more functions (transistors) per chip for the same money
  Build same products cheaper, sell the same part for less money
  Price of a transistor has to be reduced
But also want to be faster, smaller, lower power

## Slide 62: Technology Scaling
Goals of scaling the dimensions by 30%:
  Reduce gate delay by 30% (increase operating frequency by 43%)
  Double transistor density
  Reduce energy per transition by 65% (50% power savings @ 43% increase in frequency
Die size used to increase by 14% per generation
Technology generation spans 2-3 years

## Slide 63: Technology Generations

## Slide 64: Technology Evolution (2000 data)
International Technology Roadmap for Semiconductors
186
177
171
160
130
106
90
Max mP power [W]
1.4
1.2
6-7
1.5-1.8
180
1999
1.7
1.6-1.4
6-7
1.5-1.8
2000
14.9
-3.6
11-3
7.1-2.5
3.5-2
2.1-1.6
Max frequency [GHz],Local-Global
2.5
2.3
2.1
2.4
2.0
Bat. power [W]
10
9-10
9
8
7
Wiring levels
0.3-0.6
0.5-0.6
0.6-0.9
0.9-1.2
1.2-1.5
Supply [V]
30
40
60
90
130
Technology node [nm]
2014
2011
2008
2004
2001
Year of Introduction
Node years: 2007/65nm, 2010/45nm, 2013/33nm, 2016/23nm

## Slide 65: Technology Evolution (1999)

## Slide 66: ITRS Technology Roadmap Acceleration Continues

## Slide 67: Technology Scaling (1)
Minimum Feature Size

## Slide 68: Technology Scaling (2)
Number of components per chip

## Slide 69: Technology Scaling (3)
Propagation Delay
tp decreases by 13%/year
50% every 5 years!

## Slide 70: Technology Scaling (4)
From Kuroda

## Slide 71: Technology Scaling Models

## Slide 72
Scaling Relationships for Long Channel Devices

## Slide 73: Transistor Scaling (velocity-saturated devices)

## Slide 74: mProcessor Scaling
P.Gelsinger: mProcessors for the New Millenium, ISSCC 2001

## Slide 75: mProcessor Power
P.Gelsinger: mProcessors for the New Millenium, ISSCC 2001

## Slide 76: mProcessor Performance
P.Gelsinger: mProcessors for the New Millenium, ISSCC 2001

## Slide 77: 2010 Outlook
Performance 2X/16 months
  1 TIP (terra instructions/s)
  30 GHz clock
Size
  No of transistors: 2 Billion
  Die: 40*40 mm
Power
  10kW!!
  Leakage: 1/3 active Power
P.Gelsinger: mProcessors for the New Millenium, ISSCC 2001

## Slide 78: Some interesting questions
What will cause this model to break?
When will it break?
Will the model gradually slow down?
  Power and power density
  Leakage
  Process Variation