## Slide 1: Digital Integrated Circuits A Design Perspective
Designing Combinational Logic Circuits
Jan M. Rabaey
Anantha Chandrakasan
Borivoje Nikolić
November 2002.

## Slide 2: Combinational vs. Sequential Logic
Combinational
Sequential
Output =
f
(
In
)
Output =
f
(
In, Previous In
)

## Slide 3: Static CMOS Circuit
At every point in time (except during the switching
transients) each gate output is connected to either
V
DD
or
V
ss
via a low-resistive path.
The outputs of the gates assume at all times the value
of the Boolean function, implemented by the circuit
(ignoring, once again, the transient effects during
switching periods).
This is in contrast to the
dynamic
circuit class, which
relies on temporary storage of signal values on the
capacitance of high impedance circuit nodes.

## Slide 4: Static Complementary CMOS
VDD
F(In1,In2,…InN)
In1
In2
InN
In1
In2
InN
PUN
PDN
PMOS only
NMOS only
PUN and PDN are dual logic networks
…
…
Notes: One and only one of the networks (PUN or PDN) is conducting in steady state

## Slide 5: NMOS Transistors in Series/Parallel Connection
    Transistors can be thought as a switch controlled by its gate signal
    NMOS switch closes when switch control input is high

## Slide 6: PMOS Transistors in Series/Parallel Connection

## Slide 7: Threshold Drops
VDD
VDD  0
PDN
0  VDD
CL
CL
PUN
VDD
0  VDD - VTn
CL
VDD
VDD
VDD  |VTp|
CL
S
D
S
D
VGS
S
S
D
D
VGS
Notes: Why PMOS in PUN and NMOS in PDN … threshold drop
NMOS transistors produce strong zeros; PMOS transistors generate strong ones

## Slide 8: Complementary CMOS Logic Style

## Slide 9: Example Gate: NAND

## Slide 10: Example Gate: NOR

## Slide 11: Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
Notes: Shown synthesis of pull up from pull down structure

## Slide 12: Constructing a Complex Gate

## Slide 13: Cell Design
Standard Cells
  General purpose logic
  Can be synthesized
  Same height, varying width
Datapath Cells
  For regular, structured designs (arithmetic)
  Includes some wiring in the cell
  Fixed height and width

## Slide 14: Standard Cell Layout Methodology – 1980s
signals
Routing
channel
VDD
GND
Notes: Contacts and wells not shown.
What does this implement??

## Slide 15: Standard Cell Layout Methodology – 1990s
M2
No Routing
channels
VDD
GND
M3
VDD
GND
Mirrored Cell
Mirrored Cell
Notes: Contacts and wells not shown.
What does this implement??

## Slide 16: Standard Cells
Cell boundary
N Well
Cell height 12 metal tracks
Metal track is approx. 3 + 3
Pitch = repetitive distance between objects
Cell height is “12 pitch”
2
Rails ~10
In
Out
V
DD
GND

## Slide 17: Standard Cells
In
Out
V
DD
GND
In
Out
V
DD
GND
With silicided diffusion
With minimal diffusion routing

## Slide 18: Standard Cells
A
Out
V
DD
GND
B
2-input NAND gate

## Slide 19: Stick Diagrams
Contains no dimensions
Represents relative positions of transistors
In
Out
V
DD
GND
Inverter
A
Out
V
DD
GND
B
NAND2

## Slide 20: Stick Diagrams
C
A
B
X = C • (A + B)
B
A
C
i
j
j
VDD
X
X
i
GND
A
B
C
PUN
PDN
A
B
C
Logic Graph
Notes: Systematic approach to derive order of input signal wires so gate can be laid out to minimize area
Note PUN and PDN are duals (parallel <-> series)
Vertices are nodes (signals) of circuit, VDD, X, GND and edges are transitions

## Slide 21: Two Versions of C • (A + B)
X
C
A
B
A
B
C
X
VDD
GND
VDD
GND
Notes: Line of diffusion layout – abutting source-drain connections
Note crossover eliminated by A B C ordering

## Slide 22: Consistent Euler Path
j
VDD
X
X
i
GND
A
B
C
A
B
C
Notes: A path through all nodes in the graph such that each edge is visited once and only once.
The sequence of signals on the path is the signal ordering for the inputs.
PUN and PDN Euler paths are (must be) consistent (same sequence)
If you can define a Euler path then you can generate a layout with no diffusion breaks
A B C
C A B
B C A  no PDN
B A C
A C B -> no PDN
C B A

## Slide 23: OAI22 Logic Graph
C
A
B
X = (A+B)•(C+D)
B
A
D
VDD
X
X
GND
A
B
C
PUN
PDN
C
D
D
A
B
C
D

## Slide 24: Example: x = ab+cd

## Slide 25: Multi-Fingered Transistors
One finger
Two fingers (folded)
Less diffusion capacitance

## Slide 26: Properties of Complementary CMOS Gates Snapshot
High noise margins
:
V
OH
and
V
OL
are at
V
DD
and
GND
, respectively.
No static power consumption
:
There never exists a direct path between
V
DD
and
V
SS
(
GND
) in steady-state mode
.
Comparable rise and fall times:
(under appropriate sizing conditions)

## Slide 27: CMOS Properties
Full rail-to-rail swing; high noise margins
Logic levels not dependent upon the relative device sizes; ratioless
Always a path to Vdd or Gnd in steady state; low output impedance
Extremely high input resistance; nearly zero steady-state input current
No direct path steady state between power and ground; no static power dissipation
Propagation delay function of load capacitance and resistance of transistors

## Slide 28: Switch Delay Model
A
Req
A
Rp
A
Rp
A
Rn
CL
A
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
NAND2
INV
NOR2
Notes: Note capacitance on the internal node – due to the source grain of the two fets in series and the overlap gate capacitances of the two fets in series

## Slide 29: Input Pattern Effects on Delay
Delay is dependent on the pattern of inputs
Low to high transition
  both inputs go low
    delay is 0.69 Rp/2 CL
  one input goes low
    delay is 0.69 Rp CL
High to low transition
  both inputs go high
    delay is 0.69 2Rn CL
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint

## Slide 30: Delay Dependence on Input Patterns
A=B=10
A=1, B=10
A=1 0, B=1
time [ps]
Voltage [V]
Input Data Pattern | Delay (psec)
A=B=01 | 67
A=1, B=01 | 64
A= 01, B=1 | 61
A=B=10 | 45
A=1, B=10 | 80
A= 10, B=1 | 81
NMOS = 0.5m/0.25 m
PMOS = 0.75m/0.25 m
CL = 100 fF
Notes: Gate sizing should result in approximately equal worst case rise and fall times.
Reason for difference in the last two delays is due to internal node capacitance of the pulldown stack. When A transitions, the pullup only has to charge CL; when A=1 and B transitions pullup have to charge up both CL and Cint.
For high to low transitions (first three cases) delay depends on state of internal node. Worst case happens when internal node is charged up to VDD – VTn.
Conclusions: Estimates of delay can be fairly complex – have to consider internal node capacitances and the data patterns.

## Slide 31: Transistor Sizing
CL
B
Rn
A
Rp
B
Rp
A
Rn
Cint
B
Rp
A
Rp
A
Rn
B
Rn
CL
Cint
2
2
2
2
1
1
4
4
Notes: Assumes Rp = Rn

## Slide 32: Transistor Sizing a Complex CMOS Gate
OUT = D + A • (B + C)
D
A
B
C
D
A
B
C
1
2
2
2
4
4
8
8
6
3
6
6
Notes: For class lecture.
Red sizing assuming Rp = Rn
Follow short path first; note PMOS for C and B 4 rather than 3 – average in pull-up chain of three – (4+4+2)/3 = 3
Also note structure of pull-up and pull-down to minimize diffusion cap at output (e.g., single PMOS drain connected to output)
Green for symmetric response and for performance (where Rn = 3 Rp)
Sizing rules of thumb
PMOS = 3 * NMOS
1 in series = 1
2 in series = 2
3 in series = 3
etc.

## Slide 33: Fan-In Considerations
D
C
B
A
D
C
B
A
CL
C3
C2
C1
Distributed RC model
(Elmore delay)
tpHL = 0.69 Reqn(C1+2C2+3C3+4CL)
Propagation delay deteriorates rapidly as a function of fan-in – quadratically in the worst case.
Notes: While output capacitance makes full swing transition (from VDD to 0), internal nodes only transition from VDD-VTn to GND
C1, C2, C3 on the order of 0.85 fF for W/L of 0.5/0.25 NMOS and 0.375/0.25 PMOS
CL of 3.2 fF with no output load (all diffusion capacitance – intrinsic capacitance of the gate itself).
To give a 80.3 psec tpHL (simulated as 86 psec)

## Slide 34: tp as a Function of Fan-In
tpLH
tp (psec)
fan-in
Gates with a fan-in greater than 4 should be avoided.
tpHL
quadratic
linear
tp
Notes: Fixed fan-out (NMOS 0.5 micrcon, PMOS 1.5 micron)
tpLH increases linearly due to the linearly increasing value of the diffusion capacitance
tpHL increase quadratically due to the simultaneous incrase in pull-down resistance and internal capacitance

## Slide 35: tp as a Function of Fan-Out
tpNOR2
tp (psec)
eff. fan-out
All gates have the same drive current.
tpNAND2
tpINV
Slope is a function of “driving strength”
Notes: slope is a function of the driving strength

## Slide 36: tp as a Function of Fan-In and Fan-Out
Fan-in: quadratic due to increasing resistance and capacitance
Fan-out: each additional fan-out gate adds two gate capacitances to CL
tp = a1FI + a2FI2 + a3FO
Notes: a1 term is for parallel chain, a2 term is for serial chain, a3 is fan-out

## Slide 37: Fast Complex Gates: Design Technique 1
Transistor sizing
  as long as fan-out capacitance dominates
Progressive sizing
InN
CL
C3
C2
C1
In1
In2
In3
M1
M2
M3
MN
Distributed RC line
M1 > M2 > M3 > … > MN
(the fet closest to the
output is the smallest)
Can reduce delay by more than 20%; decreasing gains as technology shrinks
Notes: M1 have to carry the discharge current from M2, M3, … MN and CL so make it the largest
MN only has to discharge the current from MN (no internal capacitances)

## Slide 38: Fast Complex Gates: Design Technique 2
Transistor ordering
C2
C1
In1
In2
In3
M1
M2
M3
CL
C2
C1
In3
In2
In1
M1
M2
M3
CL
critical path
critical path
charged
1
01
charged
charged
1
delay determined by time to discharge CL, C1 and C2
delay determined by time to discharge CL
1
1
01
charged
discharged
discharged
Notes: For lecture.
Critical input is latest arriving signal
Place latest arriving signal (critical path) closest to the output

## Slide 39: Fast Complex Gates: Design Technique 3
Alternative logic structures
F = ABCDEFGH
Notes: Reduced fan-in -> deeper logic depth
Reduction in fan-in offsets, by far, the extra delay incurred by the NOR gate (second configuration).
Only simulation will tell which of the last two configurations is faster, lower power

## Slide 40: Fast Complex Gates: Design Technique 4
Isolating fan-in from fan-out using buffer insertion
CL
CL
Notes: Reduce CL on large fan-in gates, especially for large CL, and size the inverters progressively to handle the CL more effectively

## Slide 41: Fast Complex Gates: Design Technique 5
Reducing the voltage swing
  linear reduction in delay
  also reduces power consumption
But the following gate is much slower!
Or requires use of “sense amplifiers” on the receiving end to restore the signal level (memory design)
tpHL = 0.69 (3/4 (CL VDD)/ IDSATn )
= 0.69 (3/4 (CL Vswing)/ IDSATn )

## Slide 42: Sizing Logic Paths for Speed
Frequently, input capacitance of a logic path is constrained
Logic also has to drive some capacitance
Example: ALU load in an Intel’s microprocessor is 0.5pF
How do we size the ALU datapath to achieve maximum speed?
We have already solved this for the inverter chain – can we generalize it for any type of logic?

## Slide 43: Buffer Example
For given N: Ci+1/Ci = Ci/Ci-1
To find N: Ci+1/Ci ~ 4
How to generalize this to any logic path?
CL
In
Out
1
2
N
(in units of tinv)

## Slide 44: Logical Effort
p – intrinsic delay (3kRunitCunitg) - gate parameter  f(W)
g – logical effort (kRunitCunit) – gate parameter  f(W)
f – effective fanout
Normalize everything to an inverter:
ginv =1, pinv = 1
Divide everything by tinv
(everything is measured in unit delays tinv)
Assume g = 1.

## Slide 45: Delay in a Logic Gate
Gate delay:
d = h + p
effort delay
intrinsic delay
Effort delay:
h = g f
logical effort
effective fanout = Cout/Cin
Logical effort is a function of topology, independent of sizing
Effective fanout (electrical effort) is a function of load/gate size

## Slide 46: Logical Effort
Inverter has the smallest logical effort and intrinsic delay of all static CMOS gates
Logical effort of a gate presents the ratio of its input capacitance to the inverter capacitance when sized to deliver the same current
Logical effort increases with the gate complexity

## Slide 47: Logical Effort
Logical effort is the ratio of input capacitance of a gate to the input
capacitance of an inverter with the same output current
g = 1
g = 4/3
g = 5/3

## Slide 48: Logical Effort of Gates
Fan-out (h)
Normalized delay (d)
t
1
2
3
4
5
6
7
pINV
t
pNAND
F(Fan-in)
g =
p =
d =
g =
p =
d =

## Slide 49: Logical Effort of Gates
Fan-out (h)
Normalized delay (d)
t
1
2
3
4
5
6
7
pINV
t
pNAND
F(Fan-in)
g = 1
p = 1
d = h+1
g = 4/3
p = 2
d = (4/3)h+2

## Slide 50: Logical Effort of Gates

## Slide 51: Add Branching Effort
Branching effort:

## Slide 52: Multistage Networks
Stage effort: hi = gifi
Path electrical effort: F = Cout/Cin
Path logical effort: G = g1g2…gN
Branching effort: B = b1b2…bN
Path effort: H = GFB
Path delay D = Sdi = Spi + Shi

## Slide 53: Optimum Effort per Stage
When each stage bears the same effort:
Minimum path delay
Effective fanout of each stage:
Stage efforts: g1f1 = g2f2 = … = gNfN

## Slide 54: Optimal Number of Stages
For a given load,
and given input capacitance of the first gate
Find optimal number of stages and optimal sizing
Substitute ‘best stage effort’

## Slide 55: Logical Effort
From Sutherland, Sproull

## Slide 56: Example: Optimize Path
Effective fanout, F =
G =
H =
h =
a =
b =
g = 1 f = a
g = 5/3 f = b/a
g = 5/3 f = c/b
g = 1 f = 5/c

## Slide 57: Example: Optimize Path
g = 1 f = a
g = 5/3 f = b/a
g = 5/3 f = c/b
g = 1 f = 5/c
Effective fanout, F = 5
G = 25/9
H = 125/9 = 13.9
h = 1.93
a = 1.93
b = ha/g2 = 2.23
c = hb/g3 = 5g4/f = 2.59

## Slide 58: Example: Optimize Path
Effective fanout, H = 5
G = 25/9
F = 125/9 = 13.9
f = 1.93
a = 1.93
b = fa/g2 = 2.23
c = fb/g3 = 5g4/f = 2.59
g1 = 1
g2 = 5/3
g3 = 5/3
g4 = 1

## Slide 59: Example – 8-input AND

## Slide 60: Method of Logical Effort
Compute the path effort: F = GBH
Find the best number of stages N ~ log4F
Compute the stage effort f = F1/N
Sketch the path with this number of stages
Work either from either end, find sizes: Cin = Cout*g/f
Reference: Sutherland, Sproull, Harris, “Logical Effort, Morgan-Kaufmann 1999.

## Slide 61: Summary
Sutherland,
Sproull
Harris

## Slide 62: Ratioed Logic

## Slide 63: Ratioed Logic

## Slide 64: Ratioed Logic

## Slide 65: Active Loads

## Slide 66: Pseudo-NMOS

## Slide 67: Pseudo-NMOS VTC
0.0
0.5
1.0
1.5
2.0
2.5
0.0
0.5
1.0
1.5
2.0
2.5
3.0
V
in
[V]
V
o
u
t
[V]
W/L
p
= 4
W/L
p
= 2
W/L
p
= 1
W/L
p
= 0.25
W/L
p
= 0.5

## Slide 68: Improved Loads

## Slide 69: Improved Loads (2)
V
DD
V
SS
PDN1
Out
V
DD
V
SS
PDN2
Out
A
A
B
B
M1
M2
Differential Cascode Voltage Switch Logic (DCVSL)

## Slide 70: DCVSL Example

## Slide 71: DCVSL Transient Response
0
0.2
0.4
0.6
0.8
1.0
-0.5
0.5
1.5
2.5
Time [ns]
V
o
l
t
a
g
e
[V]
A B
A B
A,B
A
,
B

## Slide 72: Pass-Transistor Logic

## Slide 73: Pass-Transistor Logic

## Slide 74: Example: AND Gate

## Slide 75: NMOS-Only Logic
0
0.5
1
1.5
2
0.0
1.0
2.0
3.0
Time [ns]
V
o
l
t
a
g
e
[V]
x
Out
In

## Slide 76: NMOS-only Switch
A =
2.5 V
B
C =
2.5
V
C
L
A =
2.5 V
C =
2.5 V
B
M
2
M
1
M
n
Threshold voltage loss causes
static power consumption
V
B
does not pull up to 2.5V, but 2.5V -
V
TN
NMOS has higher threshold than PMOS (body effect)

## Slide 77: NMOS Only Logic: Level Restoring Transistor
M
2
M
1
M
n
M
r
Out
A
B
V
DD
V
DD
Level Restorer
X
• Advantage: Full Swing
• Restorer adds capacitance, takes away pull down current at X
• Ratio problem

## Slide 78: Restorer Sizing
0
100
200
300
400
500
0.0
1.0
2.0
W
/
L
r
=1.0/0.25
W
/
L
r
=1.25/0.25
W
/
L
r
=1.50/0.25
W
/
L
r
=1.75/0.25
V
o
l
t
a
g
e
[V]
Time [ps]
3.0
Upper limit on restorer size
Pass-transistor pull-down can have several transistors in stack

## Slide 79: Solution 2: Single Transistor Pass Gate with VT=0
Out
V
DD
V
DD
2.5V
V
DD
0V
2.5V
0V
WATCH OUT FOR LEAKAGE CURRENTS

## Slide 80: Complementary Pass Transistor Logic

## Slide 81: Solution 3: Transmission Gate
A
B
C
C
A
B
C
C
B
C
L
C
= 0 V
A =
2.5 V
C =
2.5 V

## Slide 82: Resistance of Transmission Gate

## Slide 83: Pass-Transistor Based Multiplexer
GND
VDD
In1
In2
S
S
S
S

## Slide 84: Transmission Gate XOR
A
B
F
B
A
B
B
M1
M2
M3/M4

## Slide 85: Delay in Transmission Gate Networks
V
1
V
i-1
C
2.5
2.5
0
0
V
i
V
i+1
C
C
2.5
0
V
n-1
V
n
C
C
2.5
0
In
V
1
V
i
V
i+1
C
V
n-1
V
n
C
C
In
R
eq
R
eq
R
eq
R
eq
C
C
(a)
(b)
C
R
eq
R
eq
C
C
R
eq
C
C
R
eq
R
eq
C
C
R
eq
C
In
m
(c)

## Slide 86: Delay Optimization

## Slide 87: Transmission Gate Full Adder
Similar delays for sum and carry

## Slide 88: Dynamic Logic

## Slide 89: Dynamic CMOS
In static circuits at every point in time (except when switching) the output is connected to either GND or VDD via a low resistance path.
  fan-in of n requires 2n (n N-type + n P-type) devices
Dynamic circuits rely on the temporary storage of signal values on the capacitance of high impedance nodes.
  requires on n + 2 (n+1 N-type + 1 P-type) transistors

## Slide 90: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (CLK = 0)
Evaluate (CLK = 1)
Notes: For class handout

## Slide 91: Dynamic Gate
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out
CL
Out
Clk
Clk
A
B
C
Mp
Me
Two phase operation
Precharge (Clk = 0)
Evaluate (Clk = 1)
on
off
1
off
on
((AB)+C)
Notes: For lecture
Evaluate transistor, Me, eliminates static power consumption

## Slide 92: Conditions on Output
Once the output of a dynamic gate is discharged, it cannot be charged again until the next precharge operation.
Inputs to the gate can make at most one transition during evaluation.
Output can be in the high impedance state during and after evaluation (PDN off), state is stored on CL
Notes: This behavior is fundamentally different than the static counterpart that always has a low resistance path between the output and one of the power rails.

## Slide 93: Properties of Dynamic Gates
Logic function is implemented by the PDN only
  number of transistors is N + 2 (versus 2N for static complementary CMOS)
Full swing outputs (VOL = GND and VOH = VDD)
Non-ratioed - sizing of the devices does not affect the logic levels
Faster switching speeds
  reduced load capacitance due to lower input capacitance (Cin)
  reduced load capacitance due to smaller output loading (Cout)
  no Isc, so all the current provided by PDN goes into discharging CL
Notes: CL being lower also contributes to power savings

## Slide 94: Properties of Dynamic Gates
Overall power dissipation usually higher than static CMOS
  no static current path ever exists between VDD and GND (including Psc)
  no glitching
  higher transition probabilities
  extra load on Clk
PDN starts to work as soon as the input signals exceed VTn, so VM, VIH and VIL equal to VTn
  low noise margin (NML)
Needs a precharge/evaluate clock

## Slide 95: Issues in Dynamic Design 1: Charge Leakage
CL
Clk
Clk
Out
A
Mp
Me
Leakage sources
CLK
VOut
Precharge
Evaluate
Dominant component is subthreshold current
Notes: leakage sources are reverse-biased diode and the sub-threshold leakage of the NMOS pulldown device.
Charge stored on CL will leak away with time (input in low state during evaluation)
Requires a minimum clock rate - so not good for low performance products such as watches (or when have conditional clocks)
PMOS precharge device also contributes some leakage due to reverse bias diode and subthreshold conduction that, to some extent, offsets the leakage due to the pull down paths.

## Slide 96: Solution to Charge Leakage
CL
Clk
Clk
Me
Mp
A
B
Out
Mkp
Same approach as level restorer for pass-transistor logic
Keeper
Notes: During precharge, Out is VDD and inverter out is GND, so keeper is on
During evaluation if PDN is off, the keeper compensates for drained charge due to leakage.
If PDN is on, there is a fight between the PDN and the PUN - circuit is ratioed so PDN wins, eventually
Note Psc during switching period when PDN and keeper are both on simultaneously

## Slide 97: Issues in Dynamic Design 2: Charge Sharing
CL
Clk
Clk
CA
CB
B=0
A
Out
Mp
Me
Charge stored originally on CL is redistributed (shared) over CL and CA leading to reduced robustness
Notes: CA initially discharged and CL fully charged.

## Slide 98: Charge Sharing Example
CL=50fF
Clk
Clk
A
A
B
B
B
!B
C
C
Out
Ca=15fF
Cc=15fF
Cb=15fF
Cd=10fF
Notes: Out = A xor B xor C
What is the worst case change in voltage on node Out - assume all inputs are low during precharge and all internal capacitances are initially 0V
Worst case is obtained by exposing the maximum amount of internal capacitance to the output node during evaluation. This happens when !A B C or A !B C
30/(30+50) * 2.5 V = 0.94 V so the output drops to 2.5 - 0.94 = 1.56 V

## Slide 99: Charge Sharing
B
=
0
Clk
X
C
L
C
a
C
b
A
Out
M
p
M
a
V
DD
M
b
Clk
M
e

## Slide 100: Solution to Charge Redistribution
Clk
Clk
Me
Mp
A
B
Out
Mkp
Clk
Precharge internal nodes using a clock-driven transistor (at the cost of increased area and power)

## Slide 101: Issues in Dynamic Design 3: Backgate Coupling
CL1
Clk
Clk
B=0
A=0
Out1
Mp
Me
Out2
CL2
In
Dynamic NAND
Static NAND
=1
=0
Notes: Due to capacitive backgate coupling between the internal and output node of the static gate and the output of the dynamic gate, Out1 voltage reduces

## Slide 102: Backgate Coupling Effect
Voltage
Time, ns
Clk
In
Out1
Out2
Notes: Out1 overshoots Vdd (2.5V) due to clock feedthrough
And Out2 never quite makes it to GND

## Slide 103: Issues in Dynamic Design 4: Clock Feedthrough
CL
Clk
Clk
B
A
Out
Mp
Me
Coupling between Out and Clk input of the precharge device due to the gate to drain capacitance. So voltage of Out can rise above VDD. The fast rising (and falling edges) of the clock couple to Out.
Notes: Danger is that signal levels can rise enough above VDD that the normally reverse-biased junction diodes become forward-biased causing electrons to be injected into the substrate.

## Slide 104: Clock Feedthrough
Clk
Clk
In1
In2
In3
In4
Out
In &
Clk
Out
Time, ns
Voltage
Clock feedthrough
Clock feedthrough

## Slide 105: Other Effects
Capacitive coupling
Substrate coupling
Minority charge injection
Supply noise (ground bounce)

## Slide 106: Cascading Dynamic Gates
Clk
Clk
Out1
In
Mp
Me
Mp
Me
Clk
Clk
Out2
V
t
Clk
In
Out1
Out2
V
VTn
Only 0  1 transitions allowed at inputs!
Notes: Out2 should remain at VDD since Out1 transitions to 0 during evaluation. However, since there is a finite propagation delay for the input to discharge Out1 to GND, the second output also starts to discharge.
The second dynamic inverter turns off (PDN) when Out1 reaches VTn.
Setting all inputs of the second gate to 0 during precharge will fix it.
Correct operation is guaranteed (ignoring charge redistribution and leakage) as long as the inputs can only make a single 0 -> 1 transition during the evaluation period

## Slide 107: Domino Logic
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PDN
In5
Me
Mp
Clk
Clk
Out2
Mkp
1  1
1  0
0  0
0  1
Notes: Ensures all inputs to the Domino gate are set to 0 at the end of the precharge period. Hence, the only possible transition during evaluation is 0 -> 1

## Slide 108: Why Domino?
Clk
Clk
Ini
PDN
Inj
Ini
Inj
PDN
Ini
PDN
Inj
Ini
PDN
Inj
Like falling dominos!

## Slide 109: Properties of Domino Logic
Only non-inverting logic can be implemented
Very high speed
  static inverter can be skewed, only L-H transition
  Input capacitance reduced – smaller logical effort
Notes: First 32 bit micro (BellMAC 32) was designed in Domino logic
Now a rather rare design style due to non-inverting logic only

## Slide 110: Designing with Domino Logic
M
p
M
e
V
DD
PDN
Clk
In
1
In
2
In
3
Out1
Clk
M
p
M
e
V
DD
PDN
Clk
In
4
Clk
Out2
M
r
V
DD
Inputs = 0
during precharge
Can be eliminated!

## Slide 111: Footless Domino
The first gate in the chain needs a foot switch Precharge is rippling – short-circuit current
A solution is to delay the clock for each stage

## Slide 112: Differential (Dual Rail) Domino
A
B
Me
Mp
Clk
Clk
Out = AB
!A
!B
Mkp
Clk
Out = AB
Mkp
Mp
Solves the problem of non-inverting logic
1 0
1 0
on
off
Notes: AND/NAND differential logic gate. The inputs and their complements come from other differential DR gates and thus all inputs are low during precharge and make a conditional transition from 0 to 1.
Annotations show state during evaluate cycle (CLK = 1)
Expensive - but can implement any arbitrary function.
Use significant power since they have a guaranteed transition every single clock cycle (regardless of signal statistics, since either Out or !Out will transition from 0 to 1).
Not ratioed (even though have a cross-coupled PMOS pair)

## Slide 113: np-CMOS
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PUN
In5
Me
Mp
Clk
Clk
Out2
(to PDN)
1  1
1  0
0  0
0  1
Only 0  1 transitions allowed at inputs of PDN Only 1  0 transitions allowed at inputs of PUN
Notes: Also called zipper logic - In4 and In5 must be from PDN’s
DEC alpha uses np-CMOS logic (Dobberpuhl)
Have to size the PUN’s to equalize the delay to that of the PDN’s
Really dense layouts and very high speed (20% faster than domino with the correct sizing)
Reduced noise margin (as with any dynamic gate)
Have two clock signals to generate and route - CLK and !CLK

## Slide 114: NORA Logic
In1
In2
PDN
In3
Me
Mp
Clk
Clk
Out1
In4
PUN
In5
Me
Mp
Clk
Clk
Out2
(to PDN)
1  1
1  0
0  0
0  1
to other
PDN’s
to other
PUN’s
WARNING: Very sensitive to noise!
Notes: NORA - no race CMOS